VoIP2ALL

Gateway

Version 1.1

# User Manual

Note:

The most updated VoIP2ALL Gateway manual is located on our Web site, at:

www.dtt.tw  in the download section. 
Check this site for latest updates.

For additional assistance please contact us:

Support Team

Discovery Telecom

Tel.: +1801 7900348
 Tel.: +7495 7907870
 Skype: discoverytelecom
 Mail:  info@dtt.tw 
 Web:  www.dtt.tw

Dear Customer,

We thank you for purchasing our VoIP2ALL Gateway.

The information in this manual does not constitute a warranty of performance, although the information has been compiled and checked for accuracy by Discovery Telecom Ltd.

All our products are developed and produced by experienced engineers, who aspire to achieve customer satisfaction, utility value and reliability of products.

Warranty Policy

The product you have purchased is under warranty of 12 months from the date of purchase, by the original purchaser. In case of defects of materials or workmanship, Discovery Telecom will replace it free of charge. This warranty applies to hardware/software but does not include SIM Cards.

This warranty will not be honored if the device has been mishandled in any way.

We hope you enjoy our product and we will be happy to receive any comments you may have. This will enable us to improve our products and the technical support that we give to every customer.

Table of Contents

User Manual	1

Getting Started	שגיאה! הסימניה אינה מוגדרת.

Check Your Package Items	7

The Dual Cell VoIP2ALL Gateway Solution Overview	8

Chapter 1: Installing SIM Cards and Connecting the Cables	9

Chapter 1.1: Installing the SIM Cards	9

Chapter 1.2: Connecting the Cables	10

Chapter 2: Installing the Manager Application	11

Chapter 2.1: Install the VoIP2ALL Management Application into an MS-Windows PC	11

Chapter 3: Configurations with the VoIP2ALL Management Application	12

Chapter 4: Port Associations	14

Chapter 4.1:General Settings 	14

Chapter 4.2: Prefixes Settings	16

Chapter 4.3: Tones Settings	18

Chapter 4.4: SIP Server Settings	שגיאה! הסימניה אינה מוגדרת.

Chapter 4.5: FXO Settings	21

Chapter 4.6: Calls Repot Records Settings	22

Chapter 4.7: SIP Status	23

Chapter 5: Users	20

Chapter 5.1: Uses Capabiliteis	20

Chapter 6: Monitoring Calls	20

Chapter 6.1: The Port Control Window	20

# Getting Started

Discovery Telecom team is glad you have chosen to use the Discovery’s Dual-Cell VoIP2ALL Gateway for your needs. We will do our best, to make your installation efforts as well as day-to-day configuration and monitoring tasks, to be as pleasant as possible. We wish you a smooth operation, while greatly saving on your office mobile phone calls.

This chapter is your “Map for installation, configuration and monitoring tasks” and includes a short explanation on each stage, as well as references for more elaborated explanations, drawings and examples in following chapters. The following is a list of tasks which are recommended to go through. It includes mandatory tasks as well as optional tasks that are not required for your current needs. It is advised, that you will use the following menu as your check-up To-Do-List. 

We advise you, to print this chapter and mark each stage when completed (e.g. V mark when done).

- Mandatory - Check package items delivered in your package

Refer to the “Check your Package Items” chapter in order to see if all items, which should be in your package, are delivered.

- Mandatory – SIM cards  installation and connections

  - Install SIM Cards

  - Install 12v Power Supply

  - Install Antennas

  - Install LAN cable

  - Install FXO connection

  - Install FXS connection

Refer to “Chapter 1: SIM Cards Installation and Cables Connecting” for specific and detailed guidelines.

- Mandatory – Install the management application

Install the MS-Windows Management Application on the PC/Laptop allocated for the system management. Use the provided CD.

Refer to “Chapter 2: Installing the Manager Application” for further information.

- Mandatory – General configurations

In order to operate the system, mandatory basic setup steps should be performed by using the LAN.

- Mandatory - System configuration

Use the LAN connection and VoIP2ALL Management MS-Windows application. You can use this method for later day-to-day management for monitoring and reports of the VoIP2ALL activity. The gateway system via IP is highly recommended as you can have the management done remotely from the system via internet connection.

# Check Your Package Items

Please verify that your package contains the following components (some were ordered specifically) before installation:

- Main Hardware Device - The  Dual Cell VoIP2ALL Gateway

- 110/220V 50-60Hz Electric Power Converter to 12V with cables supplied

- Software Installation CD - Installation kit of the Dual Cell Manager CD for MS-Windows Management Application, including the User Manual file and additional auxiliary utilities.

- 2 GSM Antennas – To be installed to the VoIP2ALL.

- LAN connection cable - for VoIP2ALL connection to the internet.

- TCP/IP Cross Cable – for connecting the gateway directly to the PC Network Interface Card.

- RS-232 Serial PC Comport connection cable (RJ-45 to RS-232 COM) – for debugging and direct access to the configuration files. Will be referred as Comport cable in this manual.

- Quick Installation Guide – for brief installation explanations.

# The Dual Cell VoIP2ALL Gateway Solution Overview

The Dual Cell VoIP2ALL Gateway, that will be referred as the VoIP2ALL in short, is a device that can operate like a small programmable IP PBX. The VoIP2ALL has a built in SIP Server that can register up to 32 VoIP clients. The Gateway can connect each of his VoIP clients to the GSM network directly completely bypasses the local landline telephone company. The VoIP2ALL has one FXS port, one FXO port, two GSM ports and a VoIP SIP Server. You can program the connection between the ports. VoIP2ALL can connect VoIP Client to another VoIP Client. You can even call from the GSM port1 to the GSM port2.

The Dual Cell can be configured to direct the calls through the most economical SIM.

# Chapter 1: Installing SIM Cards and Connecting the Cables

First you shall install the GSM SIM cards and later connect several cables and install the antennas to the VoIP2ALL Gateway.

### Chapter 1.1: Installing the SIM Cards

Insert the SIM cards into the Dual Cell as follows:

- On the bottom of the Dual Cell, open the SIM chambers by sliding the cover panels sideways.

- Open the SIM slots as follows: Position the back of the Dual Cell as shown below, grip the clip in the chamber, and slide the clip towards yourself, about ¼ cm.

- While the clip is slid towards you, pull it upward and outward. The end, closest to you, is on a hinge. Insert the SIM, so that contacts are facing down, close the clip, and close the cover panel.

### Chapter 1.2: Connecting the Cables

- LAN cable - The LAN cable is used to connect the system to the internet network, connect the LAN line to the RJ-45 as shown below.

- Antenna Cables – Connect the Antennas via antenna cables as shown below.

- FXS Cable – Connect the PBX to the FXS port as shown below.

- FXO Cable – Connect the PSTN line to the FXO port as shown below.

- 12v power cable - The device power cable is supplied with a power supply converter for covering all main voltage electricity services in the world. Connect a 120V (North America), or 240V (Europe) power supply cable to the VoIP2ALL Gateway.

# Chapter 2: Installing the Manager Application

Before operation, configuration settings must be made in the VoIP2ALL. Configuration is done on an auxiliary computer by using the VoIP2ALL Management MS-Windows Application provided for MS-Windows operating system.

### Chapter 2.1: Install the VoIP2ALL Management Application into an MS-Windows PC

1.	Insert the VoIP2ALL Management installation CD into the CD drive of the PC.

2. 	In Windows Explorer, navigate to the installation CD drive.

3.	Double click  to install the Management Application.

4.	Click Next.

5.	The Setup Type window will open.

6.	Select Complete and click next.

7.	Click Install. The VoIP2ALL Management application installs itself. Wait until a completion message will appear.

# Chapter 3: Configurations with the VoIP2ALL Management Application

After installing the Management application, launch it and define the Connection between the PC and the VoIP2ALL as described below.

Launch the VoIP2ALL Management by pressing on your PC desktop, or by pressing:

Start > Programs > Discovery Telecom > VoIP2ALL Management.

The VoIP2ALL Management application window will open.

Connecting to the Gateway

- Press  in the toolbar. The Selected Connection window will open.

- Enter in the Host Address the IP Address of the Gateway (The default IP Address is 10.16.2.245).

- Enter in the Port Number the port of the gateway (The default port is 2007).

Note: You must wait 30 seconds after connecting the power to the gateway for the initialization process to end before connecting with the PC Management.

Note: If you can't remember the IP Address see Appendix A: Com Port.

Setting the Clock

- Press  in the toolbar.

- Select in the Date box the date of the gateway.

- Enter in the Time box the time of the gateway.

- Select in the Date Format how to display the date, (Day:Month:Year) or (Year:Month:Day).

- Press Save to change the time and date.

Restarting the Gateway

To restart the gateway, press the Restart System button.

Note: This will not restart the GSM ports.

After setting the clock, define the prefixes for each port, as described in the following chapter.

# Chapter 4: Ports Associations

Communication through a VoIP2ALL is performed via ports. Each VoIP2ALL has two GSM ports, one FXS port, one FXO port and a VoIP port.  For each port you can define how to access him and what to do with calls that’s come from him.

This chapter explains the assigning of prefix to a port and the allocation of calls to the VoIP2ALL Gateway ports.

Press   to open the VoIP setup window.

Chapter 4.1: General Settings

Press the General tab to see:

Changing the IP Address of the Gateway

- Enter in the IP Address box the new IP address for the gateway.

- Enter in the Port box the new port number for the gateway.

- Press Save to activate all the changes.

- Restart the gateway, wait 30 seconds for initiation and connect with the new address.

Note: the gateway default IP address is 10.16.2.245 port 2007.

Changing the Other Settings

- Enter in the Wait for Dialing the time in seconds the gateway will wait for the first digit to be dialed.

- Enter in the Last Digit Timeout the time in seconds to wait between the last digit dialed and the calling of that number.

- Enter in the Debug Level the amount of detail to be shown on the Debug Screen.

- Press Save to activate all the changes.

Chapter 4.2: Prefixes Settings

In the basic setting, a call that’s comes in from one of the ports will receive a dial tone. The gateway will route the call according to the prefix of the dialed number.

In this window we list all the ports in the gateway and their prefixes.

Press the Prefixes tab to see:

- Enter in the Prefix box the digits that’s need to be dialed to reach the port.

  - If the prefix of a port is *, then all the calls that didn't fit the other ports prefixes will go through this port.

  - If two or more ports have the same prefix then the gateway will toggle the calls between the ports.

- Mark the Remove Prefix box to call the dialed number without the prefix digits.

- Select in the Incoming Calls Handle the operation mode for each port:

Dial Tone – All calls that come from this port will receive a dial tone to call any other port.

Blocked - All calls that come from this port will be blocked. The caller will hear a disconnected tone.

Destination Number - All calls that come from this port will Route automatically to a number according to the Incoming Calls Destination mode.

- Select in the Incoming Calls Destination how to choose the destination number:

Fixed – All calls that come from a port in a Destination Number mode will route to one fixed number according with their place in the table.

GSM1 calls will route to Num1, GSM2 will route to Num2, FXS calls will route to Num3, FXO calls will route to Num4.

Priority – All calls that come from a port in a Destination Number mode will route to Num1, if the number is busy, not answering or doesn't exist, the call will route to the next number on the list until there is a answer.

Cyclic – The same as in Priority but each call will begin in the next number in the list.

- Enter in the No Replay Timeout the number of seconds with no answer the gateway will wait before calling the next number (In Priority or Cyclic mode).

- Enter in the DELA (seconds) the number of seconds each DELA number will stay in memory.

- Press Save to activate all the changes.

Note: After you finished dialing press # to dial the number as it is without waiting the Last Digit Timeout.

Dialing from the GSM to a VoIP extension

To call VoIP from a GSM mobile phone through the GSM port 1 with the default prefix settings:

- Dial the number of the SIM card in port 1.

- Hear a dial tone.

- Dial 9 (the prefix for VoIP in this setting) and the VoIP extension number.

- Dial # to send the number.

Dialing from a VoIP extension to a GSM mobile phone

To call from a VoIP extension to GSM mobile phone through the GSM port2 with the default prefix settings:

- Pick up the VoIP extension and hear a dial tone.

- Dial 2 (the prefix for GSM port2 in this setting) and the GSM mobile number.

- Dial # to send the number.

Chapter 4.3: Tones Settings

In this window we can set the tone for each port. Where Rx is the tone of the speaker and Tx is the tone of the microphone.

Press the Tone tab to see:

Adjusting the Tones

- Press on the right side of the tone bar, a slider will appear. Slide the slider or change the level number in the middle to the desired level (From -30dbm to +30dbm).

- Repeat this action for all the tones you need to adjust.

- Press Save to activate the changes.

Chapter 4.4: SIP Server Settings

In this window we control the setting of the SIP Server.

Press the Sip tab to see:

- Press Refresh.

- Select in Codec 1 to Codec 8 the priority of the Codecs. The SIP Server will try to connect the VoIP calls using the first Codec if it isn’t possible it will try the next.

- Check the Authentication checkbox when you want that the Users will need a password to register in the gateway SIP Server.

- The SIP Port, RTP Start Port, RFC2833 Payload Type indicates the current settings of the SIP Server.

Connecting the gateway SIP Server to external SIP Server

You can connect the SIP Server of the gateway to external SIP Server by adding a host in the Hosts table. When the SIP Servers are connected you will be able to make calls from one SIP Sever to another.

Adding a Host to the Hosts Table

- Enter the Name you selected for the Host.

- Enter the IP Address of the SIP Server you want to register in.

- Enter the Port number of the SIP Server (the Default is 5060).

- Enter the User number (the number to call the Gateway in the external SIP Server).

- Enter in the Secret box the authentication number when needed.

- Press Enter.

- Press Save to update the new Hosts.

- Press the Restart Gateway button in the System Window to restart the gateway. While restarting the gateway will register in the external SIP Server.

- Connect again to the gateway.

- If the registration succeeded the Status will change to Reg.

- Go to the Prefixes window and define a prefix for this Host.

Calling to External SIP Server VoIP Client

To call a VoIP Client in the external SIP you need to dial the prefix of the Host and the number of the VoIP client.

Calling from the External SIP Server

To call the gateway from the Host you need to dial the User name, you will get a dial tone then you dial the desired number, like any other call in the gateway it will go according to the prefix of the number.

Chapter 4.5: FXO Settings

In this window we control the setting of the FXO port.

Press the FXO tab to see:

Adding a New Country to the List

- Enter in the Country Name the name of the country you want to add and press Add.

- The new country will appear on the list.

- Press on the + sign near the Dial Tone to open the Dial Tone settings of the country. Enter for each parameter the setting of the PSTN in that country.

- Do the same for the Disconnect Tone and the Ringing Tone.

- Press SAVE.

Changing the Current Country

- Select the list the Current Country for the FXO settings.

- Press SAVE.

Note: You must restart the gateway to activate the settings.

Removing a Country from the List

- Press the Remove button of the country you want to delete from the list.

- Press SAVE.

Chapter 4.6: Calls Report Records Settings

Press the CDR tab to open the window that’s control the setting of the Calls Reports.

The records of the calls are saved in files inside the gateway.

- Check the Active check box to activate the Calls Reports Records.

- Check the VoIP Filter if you don’t want to record the VoIP calls.

- Enter in the File Size box the maximum size that each CDR file could be.

- Enter in the File Amount box the maximum CDR files that would be saved in the memory.

- To see the CDR files enter in the web browser the address of the gateway, the default is: ftp://10.16.2.245/ you will see the files of the gateway, Enter the conf directory, the CDR files are in the CDR directory. Select the latest file and open it.

The CDR format is:

- Calling Number.

- Called Number.

- Origin Channel (Port number, where 33 is internal VoIP).

- Destination Channel.

- Start Time.

- Connect Time.

- End Time.

- Release Cause.

Note:  All the times is in the format [Day, Month, Year, Hour, Minute, Seconds]

Chapter 4.7: SIP Status

This window lists all the SIP Accounts that are registered in the SIP Server.

Press the Sip Status tab to see:

- Press Refresh to monitor the SIP accounts that registered in the gateway.

- The User ID is an identification number in the Sip Server for this account.

- The User Name is the sip account number.

- The User IP is the IP Address of this sip account.

Adding a New SIP account

- Open the configuration page of your SIP phone.

- Enter in the "SIP Server" parameter the IP address of the gateway.

- Enter in the "SIP User ID" parameter the number you chosen for this extension.

- If the Authentication option at the SIP tab is enabled then enter in the "Authenticate Password" the password for this client.

- Save the settings and restart.

- Press Refresh to see the SIP account in the list.

Note: For each VoIP account there must be a User in the User List. That User must have the same VoIP number as the VoIP account and the secret to match the authentication password.

# Chapter 5: Users

The identification and authorization for each action in the gateway is done by defining users. You can define up to 500 users. For each user you can define the numbers he uses and a different action for his calls.

Press   to open the Users window.

Adding a User

To add a new user to the list, Enter this values and press the Insert button:

- ID – The User number in the list.

- First Name

- Last Name

- VoIP Number

- GSM Number

- PSTN Number

- Capabilities – What this user can do.

- Active Features – Not active in this version.

- Secret – The SIP authentication password.

Updating a Number in the List

To update a user:

- Locate the user on the list.

- Change in that line the values of the user.

- Press the Update button of the user.

- Press OK to confirm update.

Deleting a User from the List

To delete a user:

- Press the Delete button of the user (located at the end of the user line in the list).

- Press OK to confirm the delete.

Searching for a User

To find a user in the list:

- Select in the Search Field box by which field to search.

- Enter the Value to search.

- Press the Search button.

- The list will show all the users that come up on the search.

- To return to the complete list press the All Users button.

5.1 The User Capabilities

DELA

The DELA is a way for a GSM mobile phone to get back to the VoIP extension that called him.

- Change the Capabilities value to 1 to enable the DELA for the user.

- When a call from the VoIP to the GSM number of the user is made, the gateway will save the number of the extension that called.

- Enter in the DELA box (in the Prefixes tab that at the VoIP window), the number of seconds the gateway will remember the extension number.

- If in that time the user will call the gateway from the GSM number, the gateway will give him a dial tone to call. He could dial any number or press * to return to the extension that called him.

- If a few extensions called the user, Pressing * will go to the first extension that called, at the next GSM call, Dialing * will go to the next extension that called.

- Each extension number will be called once.

Callback

The Callback is a way for the User to make the gateway call him and make the call on the expense of the SIM.

- Change the Capabilities value to 8 to enable the Callback for the user.

- When a call comes from the GSM number of the user, the gateway will disconnect the call and call him back.

- The user will get a dial tone to make a call.

Note: The gateway will make a callback to the user GSM number. Verify that the prefix of this number is on the prefixes table and the Remove Prefix box beside it isn’t checked.

# Chapter 6: Monitoring Calls

To monitor calls press:                          The monitor screen opens.

- The Sim indicator shows the status of the SIM (see below).

- The Net indicator shows the status of the SIM registration in the GSM network (see below).

- The SIM# indicates the number of the active SIM (From 1 to 4).

- The number at the top left indicates the GSM reception level.

- The Net ID indicates the ID number of the GSM network.

- The BCCH indicates the number of the Broadcast Channel.

The Net and Sim indicator's States:

- A red indicator indicates there is no connection.

- A yellow indicator indicates there is a connection, but no data transfer.

- A green indicator indicates transfer of data.

- Point the mouse on the blue triangle at the bottom right and click the right button. A menu will appear:

Refresh port – Get data from the ports.

Reset Port - Reset the ports, GSM port1 and GSM port2.

Port Control – Open the Port Control window.

  - The Port Control window

This window controls the GSM port settings.

- Select the SIM Number for this setting.

- Enter in the PIN Code box the PIN code of the SIM when needed.

- Select a Caller identification option in the Caller ID list:

- To enable the GSM network to set caller ID standards, select Network.

- To disable identification of the SIM, select CLIR Suppression.

- To enable identification of the SIM, select CLIR Invocation.

- To assign the SIM to work with a specific GSM network, in the Operator ID, enter the GSM network operator ID, from 1–999999. Enter 0 to work with the SIM operator.

- There are three methods of selecting the BCCH:

  - Auto BCCH Lock - The SIM will register with the BCCH with the highest RSSI.

  - BCCH Lock – Lock the SIM to register at the defined BCCH. Enter in the box the BCCH number.

  - BCCH Random – The BCCH will rotate every specified time. Select in the RSSI the BCCH minimum level of reception to register. Enter in the Timer, the time for each rotation.

- Press the BCCH Control button to monitor the BCCH cells.

- The middle cell is the cell that the SIM is connected to.

- Around it are all the surrounding BCCH cells the gateway is detecting.

- For each cell there is the following information:

- LAC - Location Area Code.

- CI - Cell ID

- MCC - Mobile Country Code

- BSIC - Basic Station Identity Code

- BCCH - Broadcast Control Channel

- RSSI- Receiver Signal Strength.

- You can choose a BCCH channel by clicking on the cell. The module will automatically register in the new BCCH.

- You can close the BCCH Control window by clicking on the X button in the middle of the window.

Sending SMS

To send SMS press the Send SMS tab:

- Select in the Format box the format of the SMS.

- Check the Right to Left box when writing in a language from right to left.

- Enter the SMS message in the Message box.

- Press the Font button to select a different font.

- Press the Save button to save the SMS.

- Enter in the Phone Number box the GSM number to send the SMS to.

- In the SMSC Number you see the number of the SMS server.

- Enter in the Bulk Numbers the list of GSM numbers, when needed to send to the SMS to many numbers.

- Press the Send button to send the SMS.

To Send SMS:

  - Write the SMS message in the Message box.

  - Enter the number to send the SMS in the Phone Number.

  - Press the Send button.

Receiving SMS

- When SMS will arrive from the GSM network an icon envelope will appear in the monitor.

- To see the messages open the SMS Inbox tab in the Port Control window.

- Press Delete to deletes the massages.

- Press the Font button to select a different font.

- Press the Save button to save the messages.

# Appendix A: Com Port

The Com Port connection, give you direct access to the Linux based operating system files of the DSP.

- Connect the Com Cable from the gateway to the PC RS232 Com Port.

- Connect the Hyper Terminal press "Disconnect" than "Properties".

- In the "Connect To" tab press "Configure", The "Port Setting" should be:

- Press "OK" and move to the Settings tab.

- Press ASCII Setup:

- Sett this settings and press OK.

- Press "Connect" in the Hyper Terminal.

- When restarting the gateway you will see the initialization process. Wait until it   finished.

- Press the Enter button. On screen you will see #.

- To see the IP settings write the command ifconfig and press Enter.

- On screen you will:

- The IP Address of the gateway is marked in a red circle.

# Text boxes

TM

Connecting VoIP 
Directly to Cell Phones

Usage Warnings

High voltage transients, surges, and other power irregularities can cause extensive damage. It is the user's responsibility to provide a power protection system.

It is the user's responsibility to install, operate, and maintain the system in accordance with all applicable codes, regulations, and safety measures.

Trademark and Patents

All trademarks, patents and copyrights apply.

General Manual Notes

Without a notice and without obligation, the contents of this manual may be revised to incorporate changes and improvements. Every effort has been made to ensure that the information is complete and accurate at the time of publication. Nevertheless, Discovery Telecom cannot be held responsible for errors or commissions.
The screen snapshots in this manual may have older version labels than your delivered package version.

IP Network

VoIP